System V Shared Memory IPC
1. Shared memory allows two or more processes to share the same region (usually referred to as a segment) of physical memory.
2. No kernel intervention is required, Hence it is the fastest IPC mechanism, on the other hand it requires user to handle the synchronisation for the shared resource, usually done with semaphores (system V/POSIX) or file locks.
3. Usage Flow
  1. Call shmget() for creating/recieving the sharem memory segment identifier.
  2. Call shmat(), which makes the segment part of the virtual memory. Access the memory with the retrieved start address.
  1. Call shmdt() for detaching memory segment (optional). This happens automatically at process termination.
  2. Call shmctl(), to destroy the memory segment. The segment will be destroyed only after all currently attached processes have detached it. Only one process needs to perform this step.

1. A child created by fork() inherits its parent’s attached shared memory segments. Thus, shared memory provides an easy method of IPC between parent and child.
2. During an exec(), all attached shared memory segments are detached.